## Slide 1: Milestone 2
By: Eric, Sunny, Tim, Eddie, and Ketan

## Slide 2: Edge Case: Two people walking in at the same time
In addition to MVS, we will use two TOF sensors mounted close to the top corners of the door
They will be mounted at an angle of 10 degrees, to determine whether a person is entering or exiting
When both TOFs trigger, we will know that two people are walking into and out of the room

## Slide 3: Edge Case 2: Person standing next to the door while another person walks out
Person in the door will block laser sensors from registering person walking in or out
The two TOF sensors alone will determine if a person is entering or exiting the room
When one of the TOF sensors is triggered and the values of distance are increasing or decreasing respectively, then the person in the room is entering or exiting

## Slide 4: Mitigation of Errors in Readings
Lots of testing to determine the best threshold for TOF sensors to register that a person is walking through the door
Create algorithm based upon these tests to determine how a series of specific distance measurements correspond to entering and exiting
TOF sensors will be set as the backup sensors in our algorithm, meaning that the laser output will be the only one used for base cases

## Slide 5: Mounting and Integration
Tripwire Sensors: Mounting using our 3D printed brackets, on the side of the door, that put the two sensors at a set distance from one another
Transmitter and Receiver for each of the sensors are also lined up through our mount
TOF sensors: Mounted using 3D printed brackets, providing TOF sensors an angle of 10 degrees, and securing each sensor close to the corners of the door

## Slide 6: Budget/Financial Status
Product | Cost
2 x E3F sensors | $18.58 * 2 = $37.16
2 TOF Sensors VL350X | $6.99
Urgenex 7.4 2200 mAh Lipo battery (x2) | $27.99
Hook and Loop Tape | $6.99
Tax + $5 per order towards the budget | $4.74 + $5.00 = $9.74
PCB + shipping | $42.14
2 x tsr 1-2450 voltage converters | $19.58
Total Cost of Materials | $150.59

## Slide 7: Plan for Financial Status
We have about $50 remaining within the budget
This can be used to purchase additional components like wires, connectors, and additional small components that will make our system easier to use
As of right now, there are no more purchases we have to make for our final system